## Slide 1: CS 31007 Autumn 2021 COMPUTER ORGANIZATION AND ARCHITECTURE
Indian Institute of Technology Kharagpur
Computer Science and Engineering
Instructors
Rajat Subhra Chakraborty (RSC)
Bhargab B. Bhattacharya (BBB)
Lecture #4:
Hardware-Software Interface: Instruction Set Architecture (ISA)
16 August 2021
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 2
Building a Computer System ……
Technology scaling (Moore’s Law)
Computing technology has scaled exponentially in performance for over half a century. This scaling was mostly the result of a virtuous cycle, where computers based on a new technology is used to create newer technology (Bootstrapping of CAD tools)
1970: 4004 P
2300 transistors

## Slide 3: Computing System Hierarchy
Compiler
Assembler
Instruction Set Architecture
Computer
Architecture
Can understand symbolic assembly
language, e.g., add C, A, B
Can understand high-level language, e.g.,
If X then C= A+B, else C= A-B
Bare Machine
(Collection of circuits)
can understand only machine language – binary strings of 0’s and 1’s, (0101001100..) i.e., electrical off and on signals (Computer Organization)
Application
software
semantic gap
Hardware-Software Interface

## Slide 4: Hardware-Software Interface
Instruction Set Architecture (ISA)
software
hardware
Courtesy: Patterson and Hennessy
ISA: Collective attributes of the machine-language instruction set;
it defines the hardware-software interface

## Slide 5: Hardware Hierarchy
CPU, RAM, Control, I/O
Flip-flops (memory), Registers,
Logic circuits
Logic gates – AND, OR, NAND
Transistors
(Semiconductor switches)
bare machine
Wiring (interconnections), I/O pads, clocks, power

## Slide 6: How a program is executed by a computer
Application software,
a program in C:
swap (int v[ ], int k)
{int temp;
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}
Compiler
Assembler
See pages 122-123
Compiler translates it to
assembly language program
of the target machine
swap;
muli $2, $5, 4
add $2, $4, $2
lw $15, 0 ($2)
lw $16, 4 ($2)
sw $16, 0 ($2)
sw $15, 4 ($2)
jr $31
binary machine code
00000000101000010000000000011000
00000000000110000001100000100001
10001100011000100000000000000000
10001100111100100000000000000100
10101100111100100000000000000000
10101100011000100000000000000100
00000011111000000000000000001000
Hardware
output

## Slide 7: Below Your Program
Application software
  Written in high-level language
System software
  Compiler: translates HLL code to machine code
  Operating System: service code
    Handling input/output
    Managing memory and storage
    Scheduling tasks & sharing resources
Hardware
  Processor, memory, I/O controllers
§1.3 Below Your Program

## Slide 8: Levels of Program Code
High-level language
  Level of abstraction closer to problem domain
  Provides for productivity and portability
Assembly language
  Textual representation of machine instructions
Hardware representation
  Binary digits (bits)
  Encoded instructions and data

## Slide 9: Program Execution
Assembler
Compilier
Hardware
Program written in high-level language, e.g., C
Assembly-language code
Machine-language code (binary)
Questions:
Where is the compiler running?
Who compiles the compiler?
How is the Assembler running?
Result

## Slide 10: System Hierarchy
Application Software
Algorithms
Applications
Instruction Set Architecture (ISA)
System Software
Operating Systems, Compilers
Programming Language
Bare Machine
(Hardware)
Gates/Register-Transfer Level (RTL)
Microarchitecture
Devices - Transistors
Physics
Circuits – Gates, Flip-flops

## Slide 11
Computer Organization versus Computer Architecture
Computer Organization (bottom-up view)
  The actual implementation of components in hardware
Computer Architecture (top-down view)
  The view of a computer as perceived by software designers
Instruction Set Architecture (ISA)

## Slide 12
Computer Organization versus Computer Architecture
Computer Organization:
  The anatomy of a machine
  (structural view)
Computer Architecture: The personality of a machine
(behavioral view)
Instruction Set Architecture (ISA)

## Slide 13: Computer Architecture
Architecture is visible to a programmer
  Instruction set
  Registers
  Data representation, addressing modes
  I/O mechanisms
  Virtual view of memory

## Slide 14: Computer Organization
Organization is visible to hardware designer
  Hardware implementation of an instruction
  Registers, program counter
  Arithmetic and logical units
  Control logic, internal states
  Pipelining hardware
  Cache and main memory

## Slide 15: Computer Design Approach
Instruction Set Architecture (ISA)
System software
(OS, Compiliers)
Computer Organization
Bottom-up approach:
Hardware first, ISA later
Instruction Set Architecture (ISA)
System software
(OS, Compiliers)
Computer Organization
Top-down approach:
ISA first, hardware later

## Slide 16: Instruction Set Architecture (ISA)
A set of assembly language instructions that separates the interface between software and hardware
In top-down design, given an ISA, an appropriate hardware platform is built to support it
Based on ISA, OS and compilers are to be developed accordingly further going up
Once ISA is fixed, software and hardware engineers can work independently (start from the middle!)
ISA is designed to optimize the performance supported by the available hardware technology.

## Slide 17: The Hardware of a Computer
Central Processing Unit (CPU)
I/O devices
Memory
Control
ALU
Registers
Five easy pieces:
Control, Arithmetic Logic Unit (ALU), Memory, Input/Output, Datapath (Bus)

## Slide 18: Digital System Design from Three Perspectives
Gajski-Kuhn Y-Chart (1983)
: Computer
Organization
Computer
Architecture
: VLSI Design

## Slide 19: Factors behind the exponential growth of computing paradigms
Evolution of computer architecture
Growth of semiconductor technology and IC design processes
Memory technologies
Algorithms and data structures
Programming languages, compilers, OS
Test, verification, error management techniques
Bootstrapping: using present computers to design the next generation of computers (design automation)
Parallel and distributed computing
Networking, Cloud, IoT

## Slide 20: First Computer Built in India
In 1966, a fully-transistorized, digital computer named ISIJU was designed and commissioned, with joint collaboration between Indian Statistical Institute (ISI) and Jadavpur University (JU), Kolkata
In 1953, S K. Mitra designed and constructed the first (analog) computer built in India for solving linear equations with ten variables and related problems
Mountain View, CA
Commemoration plaque at the Computer History Museum, Mountain View, California, USA

## Slide 21: CS 31007 Autumn 2021 COMPUTER ORGANIZATION AND ARCHITECTURE
Indian Institute of Technology Kharagpur
Computer Science and Engineering
Instructors
Rajat Subhra Chakraborty (RSC)
Bhargab B. Bhattacharya (BBB)
Lecture #5, #6:
17 August 2021
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 22: Next Agenda
Model for computation and Turing Machine
von Neumann Architecture
Basic Features of Instruction Set Architecture (ISA)
CPU Performance Equation
Amdahl’s Law; Gustavson-Barsis Law
RISC versus CISC
Die yield
Notes: Good Morning!
The title of today’s talk is “On some Planar Partitioning Problems”.

## Slide 23
Three Challenges
1. How to design compact, efficient, and reliable hardware (logic)?
2. What is the simplest, yet all powerful computer (computability)?
3. How should the basic computer architecture be conceived (mechanism for executing instructions)?

## Slide 24: Pioneers who answered these three questions
John von Neumann (1903-1957)
Alan Turing
(1912-1954)
Claude E. Shannon (1916-2001)
Logic design
(basis of computer organization; hardware cost/ circuit delay/power optimization)
Theory of computability (basis for the fundamental requirement in computation)
Blueprint for basic computer architecture
Claude E. Shannon: A Symbolic Analysis of Relay and Switching Circuits, Master’s Thesis, MIT, 1937

## Slide 25
Alan Turing, who gave the fundamental abstraction of a computing machine, was an excellent long distance runner
Pioneer of theoretical computer science and artificial intelligence
His father served in Indian Civil Service and worked in Odisha
Turing Machine

## Slide 26
What is the simplest yet all powerful computer?
Alan Turing (1936): Conceived a machine that introduces a model for computation (Turing Machine)
Finite-State Control
Read/Write Head
L
R
Infinite Tape
$ 0 1 0 B 1 M 0 $
symbols (input, tape, blank)
The tape head can move left or right
Actions: (present state, current symbol) 
(new state, write symbol, move one cell left/right);
-- The machine halts when an “accept”/”reject” state
is reached

## Slide 27
Turing Machine
Very simple mechanism:
-- memory, control, read/write, shift, accept/reject
A. M. Turing (1936) , On Computable Numbers with an Application to the Entscheidungsproblem, Proc. Royal Math. Soc., Ser. 2, Vol. 42, pp. 230-265, 1936.
Extremely powerful
Church-Turing Conjecture (1936): A function on natural numbers can be calculated by an effective method if and only if it is computable by a Turing machine
Any procedure that is computable by paper-and-pencil methods (algorithm) can be solved by a Turing machine

## Slide 28
Some Fundamental Limitations
Albert Einstein (1905):
Special theory of relativity  elimination of the notion of absolute time (postulate: the velocity of light is constant)
Kurt Gödel (1931):
Incompleteness theorem  questioned the notion of absolute mathematical truth
Alan Turing (1936):
Halting problem of Turing Machine  algorithmic inability to identify the presence of an infinite loop in arbitrary programs

## Slide 29
Halting Problem: Can we write a program Q, which given any arbitrary program P as input, will decide whether on not P terminates or falls into an infinite loop on some input data?
Turing Undecidability?
Halting problem is Turing undecidable

## Slide 30: Gödel’s Incompleteness Theorem
In 1931, Gödel demonstrated that within any given branch of mathematics, there would always be some propositions that cannot be proven either true or false using the rules and axioms
Kurt Gödel
1906-1978

## Slide 31
“What we want is a machine that can learn from experience”
- Alan Turing
Father of AI/Machine Learning?

## Slide 32
Stored program concept
Serves as the basis for almost all modern computers
Instructions and data are just bits
Programs (sequence of machine instructions) are stored in memory to be read or written just like data
memory for data, programs,
compilers, systems programs
von Neumann Architecture (1945): Princeton Architecture
Processor
Memory
Registers
Fetch & Execute Cycle (Instruction Cycle)
  Program Counter (PC) points to the next Instruction to be fetched
  Specific bits (opcode field) in the Instruction "control" subsequent actions
  Fetch the “next” instruction and continue
PC

## Slide 33
X = - 1,880,113,152 (if X is a 2’s complement binary number)
X = 2,414,854,144 (when X is an unsigned binary number)
X = - 1.873 × 2-96 (when X is a floating-point number)
X lw $t7, -16384 ($ra) (when X is a MIPS instruction)
Let the content (X) of a memory location be:
X: 0x 8FEFC000
X: 1000 1111 1110 1111 1100 0000 0000 0000
Binary String Stored in Memory: Who am I?
Processor
Memory
Registers
  Need execution cycles to interpret the binary strings properly – whether it is instruction or data, and if data, what type?
PC

## Slide 34: Execution Cycle a.k.a. Instruction Cycle
Instruction
Fetch (IF)
Obtain instruction from memory
Instruction
Decode (ID)
Determine required actions and instruction size
Operand
Fetch (Mem)
Locate and obtain operand data from memory/register (Mem)
Execute (EX)
Compute result value or status (Execute)
Result
Store (WB)
Deposit results in register/memory for later use (Write Back)
Next
Instruction
Determine successor instruction
(Program Counter points to next instruction; next sequential memory address or branch targets)

## Slide 35: Features of von Neumann Architecture
Same physical memory to save instructions and data
Instruction fetch and data transfer cannot be done concurrently; they need separate clock cycles
Simple architecture
Harvard Architecture: Separate instruction and data memory

## Slide 36: Harvard Architecture
CPU
Control
ALU
Instruction
memory
Data
memory
I/O devices
Based on Harvard Mark I relay-based computer model
Separate signal pathways for instruction and data; can be accessed concurrently

## Slide 37: Full Picture
Processor
Control
Datapath
Memory
for storing
instructions and data
Devices
Input
Output
Monitor
Printer
Keyboard
Mouse
ALU
Notes: 1. The input devices bring the object code and input data from the outside world into the computer.

## Slide 38: Next ..
How programs are translated into the machine language
  And how the hardware executes them
The hardware/software interface
What determines program performance
  And how it can be improved
How hardware designers improve performance
How parallel processing helps

## Slide 39: How machine-language programs are executed?
Processor
Control
Datapath
Memory
Devices
Input
Output
000000 00000 00101 0001000010000000
000000 00100 00010 0001000000100000
100011 00010 01111 0000000000000000
100011 00010 10000 0000000000000100
101011 00010 10000 0000000000000000
101011 00010 01111 0000000000000100
000000 11111 00000 0000000000001000
Load Input Binary
Notes: 1. The input devices bring the object code and input data from the outside world into the computer.

## Slide 40: Code Stored in Memory
Processor
Control
Datapath
Memory
Devices
Input
Output
000000 00000 00101 0001000010000000
000000 00100 00010 0001000000100000
100011 00010 01111 0000000000000000
100011 00010 10000 0000000000000100
101011 00010 10000 0000000000000000
101011 00010 01111 0000000000000100
000000 11111 00000 0000000000001000
Notes: 2. These data are kept in the computer’s memory until ...
Note that memory holds both INSTRUCTIONS and DATA and you can’t tell the difference. They are both just 32 bit strings of zeros and ones.

## Slide 41: Processor Fetches an Instruction
Processor
Control
Datapath
Memory
Devices
Input
Output
000000 00000 00101 0001000010000000
000000 00100 00010 0001000000100000
100011 00010 01111 0000000000000000
100011 00010 10000 0000000000000100
101011 00010 10000 0000000000000000
101011 00010 01111 0000000000000100
000000 11111 00000 0000000000001000
Processor fetches an instruction from memory
pointed by Program Counter PC
Where does it fetch from?
PC
instruction
data
Notes: 3. The processor request and process them.

## Slide 42: Control Decodes the Instruction
Processor
Control
Datapath
Memory
Devices
Input
Output
000000 00100 00010 0001000000100000
Control decodes the instruction to determine what to execute
Notes: 3. The processor control decodes the instruction in order to figure out what to tell the datapath to do

## Slide 43: Datapath Executes the Instruction
Processor
Control
Datapath
Memory
Devices
Input
Output
contents Reg #4 ADD contents Reg #2
results put in Reg #2
Datapath executes the instruction as directed by control
000000 00100 00010 0001000000100000
Notes: 4. The operation of the datapath is controlled by the processor’s controller.

## Slide 44: What Happens Next?
Processor
Control
Datapath
Memory
Devices
Input
Output
000000 00000 00101 0001000010000000
000000 00100 00010 0001000000100000
100011 00010 01111 0000000000000000
100011 00010 10000 0000000000000100
101011 00010 10000 0000000000000000
101011 00010 01111 0000000000000100
000000 11111 00000 0000000000001000
Fetch
Decode
Exec
Notes: For lecture
3. What happens next (next instruction is fetched/how to tell where that instruction is located in memory/…)

## Slide 45: Output Data Stored in Memory
Processor
Control
Datapath
Memory
Devices
Input
Output
00000100010100000000000000000000
00000000010011110000000000000100
00000011111000000000000000001000
On program completion, results reside in memory
Notes: 5. The data to be output are kept in the computer’s memory until ...

## Slide 46: Output Device Outputs Data
Processor
Control
Datapath
Memory
Devices
Input
Output
00000100010100000000000000000000
00000000010011110000000000000100
00000011111000000000000000001000
Notes: 1. The output device outputs the data in the memory to the output medium.

## Slide 47: Von Neumann Bottleneck
Von Neumann architecture uses the same memory for instructions (program) and data.
Memory is inherently slower than logic. The time spent in memory accesses can limit the performance. This phenomenon is referred to as von Neumann bottleneck.
To avoid the bottleneck, later architectures allow frequently used operands to reside in on-chip registers, or use cache.

## Slide 48
Complete View of Computer Architecture
On-chip cache
Cache Memory
(SRAM)
Secondary Memory (Flash, Hard disk, SSD, CD)
Tertiary Memory (Tape, RAID, Data centres, Network)
Use of memory hierarchy
reduces the transaction time
across CPU-memory interface
Control
Datapath
ALU
Registers
Processor (CPU)
Main Memory (DRAM)
Memory

## Slide 49
Memory Hierarchy (MH)
MH reduces average CPU-Memory transaction time;
need additional hardware, OS (memory management)
speed, cost
storage
capacity
CPU

## Slide 50: Components of a Computer
Same components for all kinds of computer
  Desktop, server, embedded
Input/output includes
  User-interface devices
    Display, keyboard, mouse
  Storage devices
    Hard disk, CD/DVD, flash
  Network adapters
    For communicating with other computers
§1.4 Under the Covers
The BIG Picture

## Slide 51: Touchscreen
PostPC device
Supersedes keyboard and mouse
Resistive and Capacitive types
  Most tablets, smart phones use capacitive
  Capacitive allows multiple touches simultaneously

## Slide 52: Through the Looking Glass
LCD screen: picture elements (pixels)
  Mirrors content of frame buffer memory

## Slide 53: Opening the Box
Capacitive multitouch LCD screen
3.8 V, 25 Watt-hour battery
Computer board

## Slide 54: Inside the Processor (CPU)
Datapath: performs operations on data
Control: sequences datapath, memory, ...
Cache memory
  Small fast SRAM memory for immediate access to data

## Slide 55: Inside the Processor
Apple A5

## Slide 56: A Safe Place for Data
Volatile main memory
  Loses instructions and data when power off
Non-volatile secondary memory
  Magnetic disk
  Flash memory, SSD
  Optical disk (CDROM, DVD)

## Slide 57: Networks
Communication, resource sharing, nonlocal access
Local area network (LAN): Ethernet
Wide area network (WAN): the Internet
Wireless network: WiFi, Bluetooth

## Slide 58: Technology Trends
Electronics technology continues to evolve
  Increased capacity and performance
  Reduced cost
DRAM capacity
§1.5 Technologies for Building Processors and Memory

## Slide 59: Instruction Set Architecture (ISA)
The set of machine-level instructions in a particular CPU implementation is called Instruction Set
Goals of Instruction Set:
  Software must be able to compute anything in a reasonable number of steps using the instructions in the instruction set
Different CPUs implement different sets of instructions

## Slide 60: Features of Instruction Set Architecture (ISA)
Instruction format: length (how many bits – fixed or variable?), format, fields, opcodes, register specifications, how many operands/memory addresses specified?
Size of the logical address space? Addressability (byte/word level)?
Number of instructions? – determines #bits in op-code.
Instruction types? – arithmetic (integer/floating point), logical, data transfer, branch, procedure calls, bit-shifting
Addressing modes: immediate, direct, register, displacement, scaled, indirect; addressing granularity (word-level, byte-level?)
Others: Orthogonality, Completeness, Alignment (Big-Endian/Little-Endian)
ISA governs both hardware implementation (downward) and compiler design (upward)

## Slide 61: Example: MIPS ISA
The length of every instruction = 32 bits
Memory is byte-addressable, word-organized, each word comprising 4 bytes = 32 bits
Width of the address bus: 32 bits; size of the logical address space = 2^32 bytes =2^30 words
32 on-chip general purpose registers, each 32-bit wide; register-ID needs 5 bits each
Integers, FP-numbers: 32 bits
Op-code in each instruction: 6 bits
-------------------------------------------------------------------------------------------------------------
MIPS: Microprocessor without Interlocked Pipeline Stages (RISC Computer, 1986)
MIPS: Million Instructions Per Second (Performance)

## Slide 62: Example: MIPS Instruction
Collection of Assembly-level or Machine-level (M/L) instructions, which are executable by the hardware
An example of MIPS M/L instruction:
Total length of the instruction – 32 bits; opcode: 6 bits;
$t0, $s1 -> 32-bit CPU registers (ID: 5-bit each, as there are a total of 32 such registers); immediate value is provided as a 16-bit 2’s complement integer;
Add 5 to the content of $s1 and save the result in $t0
op
s1
t0
Immediate
6 bits
5 bits
5 bits
16 bits
addi $t0, $s1, 5
001000
10001
01000
0000000000000101

## Slide 63
MIPS Load Instruction
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
lw $t1 - 40($t2)
Processor
Memory
Registers
PC
Meaning of lw $rt imm($rs):
R[rt]  Mem{R[rs] + Sign_Ext(imm16)}
MIPS is based on load-store architecture: instructions are broadly classified as two types - memory access (load and store between external memory and registers) and ALU operations (occurring only among internal registers)
16-bit 2’s complement number representing the immediate (offset) value

## Slide 64: Immediate Operands
Constant data specified in an instruction
addi $s3, $s3, 4
No subtract immediate instruction
  Just use a negative constant
  addi $s2, $s1, -1
Design Principle 3: Make the common case fast
  Small constants are common
  Immediate operand avoids a load instruction, which memory access

## Slide 65: Arithmetic Operations
Add and subtract, three operands
  Two sources and one destination
add a, b, c # a gets b + c
All arithmetic operations have this form
Design Principle 1: Simplicity favours regularity
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost
§2.2 Operations of the Computer Hardware

## Slide 66: Register Operands
Arithmetic instructions use register operands
MIPS has a 32 × 32-bit register file
  Use for frequently accessed data
  Numbered 0 to 31
  32-bit data called a “word”
Assembler names
  $t0, $t1, …, $t9 for temporary values
  $s0, $s1, …, $s7 for saved variables
Design Principle 2: Smaller is faster
  Compare to: main memory  millions of locations
§2.3 Operands of the Computer Hardware

## Slide 67: Register Operand Example
C code:
f = (g + h) - (i + j);
  f, …, j in $s0, …, $s4
Compiled MIPS code:
add $t0, $s1, $s2 add $t1, $s3, $s4 sub $s0, $t0, $t1

## Slide 68: Memory Operands
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers
  Store result from register to memory
Memory is byte addressed
  Each address identifies an 8-bit byte
Words are aligned in memory
  Address must be a multiple of 4; PC <- PC +4
MIPS is Big Endian
  Most-significant byte at least address of a word
  c.f. Little Endian: least-significant byte at least address

## Slide 69: Registers vs. Memory
Registers are faster to access than memory
Operating on memory data requires loads and stores
  More instructions to be executed
Compiler must use registers for variables as much as possible
  Only spill to memory for less frequently used variables
  Register optimization is important!

## Slide 70: Performance Issues -- CPU-Performance Equation -- Amdahl’s Law

## Slide 71: What Affects Performance?
Algorithm
  Determines number of operations executed
Programming language, compiler, architecture
  Determine number of machine instructions executed per operation depends on ISA
Processor and memory system
  Determine how fast instructions are executed
I/O system (including OS)
  Determines how fast I/O operations are executed

## Slide 72: Response Time and Throughput
Response time
  How long it takes to do a task
Throughput
  Total work done per unit time
    e.g., tasks/transactions/… per hour
How are response time and throughput affected by
  Replacing the processor with a faster version?
  Adding more processors?
We’ll study their estimation

## Slide 73
Response time: time between submission of a job (program P) and its completion (depends on overall system load)
This includes
--- I/O
--- Operating system time for managing programs, compile time, etc.
--- CPU-time includes time for executing the machine code for P, memory access time, procedure calls, and system time spent on P.
Performance is proportional to the inverse of the CPU time.

## Slide 74: What determines the execution time of a machine/assembly-level program P when it is run on a machine M?
P consists of a number of machine-level instructions (IC: instruction count);
Each machine instruction requires several clock cycles to complete (CPI: average number of clock cycles per instruction);
Each clock cycle has certain time period (CCT: clock cycle time)
Thus, CPU-time = IC  CPI  CCT
(CPU Performance Equation)

## Slide 75
ALU-op: 40%, Clock-cycles needed = 1
load-op: 20%, Clock-cycles needed = 2
store-op: 10%, Clock-cycles needed = 2
branch-op: 30%, Clock-cycles needed = 2
Hence CPI = 1*0.4 + 2*0.2 + 2*0.1 + 2*0.3
= 1.60